Building Owner:								Inspector Name:

Building Address:								Inspector Address:

Notes:

Air Barrier and Insulation Inspection Component Criteria Checklist

| Component | Criteria | Date | Inspector |
| --- | --- | --- | --- |
| Air barrier and thermal barrier | Exterior thermal envelope insulation for framed walls is installed in substantial contact and continuous alignment with building envelope air barrier. |  |  |
|  | Breaks or joints in the barrier are filled or repaired. |  |  |
|  | Air-permeable insulation is not used as a sealing material. |  |  |
|  | Air-permeable insulation is inside of an air barrier. |  |  |
| Ceiling/attic | Air barrier in any dropped ceiling/soffit is substantially aligned with insulation and any gaps are sealed. |  |  |
|  | Attic access (except unvented attic), knee wall door, or drop down stair is sealed. |  |  |
| Walls | Corners and headers are insulated. |  |  |
|  | Junction of foundation and sill plate is sealed. |  |  |
| Windows and doors | Space between window/door jambs and framing is sealed. |  |  |
| Rim joists | Rim joists are insulated and include an air barrier. |  |  |
| Floors (including above garage and cantilevered floors) | Insulation is installed to maintain permanent contact with underside of subfloor decking. |  |  |
|  | Air barrier is installed at any exposed edge of insulation. |  |  |
| Crawl space walls | Insulation is permanently attached to walls. |  |  |
|  | Exposed earth in unvented crawl spaces is covered with Class I vapor retarder with overlapping joints taped. |  |  |
| Shafts, penetrations | Duct shafts, utility penetrations, knee walls and flue shafts opening to exterior or unconditioned space are sealed. |  |  |
| Narrow cavities | Batts in narrow cavities are cut to fit, or narrow cavities are filled by spray/blown insulation. |  |  |
| Garage separation | Air sealing is provided between the garage and conditioned spaces. |  |  |
| Recessed lighting | Recessed light fixtures are air tight, IC rated, and sealed to drywall. Exception – fixtures in conditioned space. |  |  |
| Plumbing and wiring | Insulation is placed between outside and pipes. Batt insulation is cut to fit around wiring and plumbing, or sprayed/blown insulation extends behind piping and wiring. |  |  |
| Shower/tub on exterior wall | Showers and tubs on exterior walls have insulation and an air barrier separating them from the exterior wall. |  |  |
| Electrical/phone box on exterior walls | Air barrier extends behind boxes or air sealed-type boxes are installed. |  |  |
| Common wall | Air barrier is installed in common wall between dwelling units. |  |  |
| HVAC register boots | HVAC register boots that penetrate building envelope are sealed to subfloor or drywall. |  |  |
| Fireplace | Fireplace walls include an air barrier. |  |  |

Modified: 08/26/2011